## Slide 1: Question 1
CSAP Special Projects Update
Emerging Issues - Soil Relocation
Current State of Practice –
Issues and Uncertainty
Project Lead:
Jeff Taylor, Core 6 & Mike Geraghty, Keystone Environmental
Notes: BC is roughly 20 times the size of the Netherlands
Based on an inventory conducted in 2004 in the Netherland, there were approximately 425K potentially contaminated sites in the Neth., this number was reduced (through inv and rem) to approximately 260,000 by 2009
According to the BC Site Registry database, there are approximately XXX registered sites in BC
The Netherlands has a very long history of industrial use dating back to the Industrial Revolution in the 1700’s, whereas in BC, industrial development began later around the 1850’s, and to this day remains localized to major centers with large quantities of undeveloped lands remaining.
Based on the information presented by Yvo, the first true soil protection standards came into force in January 1983. In BC, of course, the CSR came in nearly 14 years later in Dec 1996, which gives the Dutch a bit of a head start compared to BC, but not as much as you might think, given their history

## Slide 2: Presentation Outline
Background
Specific Scenarios
Considerations
Questions

## Slide 3: Background
Schedule 7 repealed as part of CSR Omnibus Update
  CSR Section 46 revised as part of CSR Omnibus Update
    Section 46.1: Soil can be relocated without a CSRA if it meets the lowest numerical soil and vapour standard for the receiving site.
    Section 46.2: Can use leachate testing as an alternate if soil exceeds groundwater protection matrix standards.
  Pending regulatory and policy changes outlined in ENV document: Final Policy Direction – Prevention of Contamination from Soil Relocation, January 2019.

## Slide 4: Scenario 1 – pH Amendment
Soil with a low pH exceeds pH dependent standards for certain metals at the source site.
Can that soil be relocated directly to a receiving site with a higher pH where the metals concentrations would not exceed the standards or would the pH of the source site soil need to be amended to alter the pH to match that of the receiving site prior to relocation?

## Slide 5: Scenario 1 – pH Amendment
Recommendation: This should be permitted without amendment as the pH of the receiving site should stabilize any metals that may leach out of the lower pH relocated soil.
Volume of relocated soil should be considered with respect to the size of the receiver site and the capacity to buffer the relocated soils.

## Slide 6: Scenario 2 – pH variability at a Site
An industrial site has an upland portion comprised of till and a lowland portion with peat soils that is 2m lower in elevation. The owner wants to level the site with imported fill material and raise the overall grade by 1 m. The peat soils have an average pH of <5 and the till soils have an average pH of >7.5.
Using TG-5, the median pH (accounting for 2 terrain types) is currently considered. Assuming median pH is still <6:
Would it be permissible to relocated soils with pH dependent metals (e.g. Lead) that only meet the standard for the higher pH at the till portion to be relocated only to the till portion of the site?

## Slide 7
Recommendation: The locations of the different soil types would need to be documented by a qualified professional and the records retained on file. The receiver site boundary should be defined as the till-area using a metes and bounds description.
Lead in Soil |  |  |  | 
Soil Location |  | pH | Applicable CSR Standard (mg/kg) | Concentration (Pb - mg/kg)
Generator |  | 5.9 | 150 | 500
Receiver | Peat | 4.5 | 120 | Exceeds
 | Till | 7.8 | 1000 | Within Standard

## Slide 8: Scenario 3 – AW to BCWQG transition
A receiving site is located adjacent to a surface water body and the soil is to be placed within 10m of the water body to raise the elevation for flood protection.
Given that groundwater within 10m of a receiving aquatic environment must meet BC Water Quality guidelines, how is the matrix standard for aquatic life groundwater protection standards to be evaluated?
Can the existing AW protection matrix standards be used or must the soil undergo a leachate test and the leachate be compared to BC WQG?

## Slide 9
Recommendation: A leachate test be compared to BC WQG.

## Slide 10: Scenario 4 - Salt-Impacted Soil used for Diking
Salt contaminated soil, generated from a road widening project in Delta, is proposed for use as diking material, adjacent to a marine foreshore.
  Applicable standards at the source site include those for IW and DW matrices.
  Salt contamination related to ingress of saline water into nearby irrigation ditch network.
  Receiver site is adjacent to marine foreshore but may have an underlying freshwater aquifer and irrigation ditches are situated nearby.
  TG-20 only applies to dredgate.
Recommendation: This activity should be permitted in accordance with the spirit of TG-20.

## Slide 11: Other Considerations
  Climate change is resulting in sea level rise and need for ongoing flood control measures – diking and/or increasing construction elevation. This will mean significant soil relocation in the future.
Agricultural Land Commission must approve all non-agricultural land uses, including soil removal and deposit.
Local Governments have authority to regulate soil removal and deposit by way of permits and fees.
Contaminated Soil Relocation Agreements no longer supported by ENV.
Risk-based relocation no longer supported by ENV.